## Slide 1
A Local-Ratio-Based Power Control Approach for Capacitated Access Points in Mobile Edge Computing
Qinghui Zhang, Weidong Li, Qian Su, Xuejie Zhang*
Yunnan University
zhangqinghui@mail.ynu.edu.cn, {weidong, suqian, xjzhang}@ynu.edu.cn

## Slide 2
Background
01
Experiments
03
Our Approach
02
Conclusion
04

## Slide 3
With the rapid development of beyond 5G/6G and the Internet of Things, increasing number of terminal devices (TD) are being deployed at the edge of networks.
A TD usually establishes network connection with edge server through its access point (AP).
Larger signal coverage disk needs more power
Background

## Slide 4
Task: Determine the power assignment in MEC such that APs with limited capacity can cover all TDs and minimize the total power. We define this problem as the minimum power capacitated cover (MPCC) problem.
Challenges: MPCC is a fundamental minimum power coverage (MPC) problem. It’s challenging to solve optimally even without capacity constraints.
Background

## Slide 5
Related Work
MPC
minimum power cover
MWSC
minimum weight set cover
MPPC
Minimum power partial cover
MPCC
minimum power capacitated cover
SC
set cover
Different power control method for different wireless networks:
Cellular Network
  Sum Spectral Efficiency (SE), Maximize system sum-rate
Wireless Sensor Network
  Lowest transmission power to respect quality requirements
Set Cover

## Slide 6
Motivation
Power control for wireless signal transmission, considering the limited resources of edge servers, is a considerable research topic.
The minimum power cover problem has rarely been considered for capacity constraints.

## Slide 7
Our Contribution
MPCC and Resource Allocation Model
Local-Ratio-Based Algorithm
Performance Evaluation

## Slide 8
Background
01
Experiments
03
Our Approach
02
Conclusion
04

## Slide 9
System Model
Two facilities:
  APs with same capacity
  TDs
Power formula
Disk definition
  𝑎 and 𝑢 ∈ 𝑈 can determine a unique disk 𝐷𝑎𝑢, so at most disks must be considered and denoted it by 𝒟.
  To simplify the notation, we use 𝐷 to represent both a disk in 𝒟 and the set of TDs contained in
2

## Slide 10
Integer Program
Full coverage condition: , denotes the TDs covered by ; then must be established.
Limited capacity condition: The number of TDs covered by an AP must be less than its capacity.
Power uniqueness: there is at most one disk with 𝑎 as the center in .
For a subset of 𝒟, is a feasible solution to the MPCC problem and must meet the following conditions:

## Slide 11
Minimum Local Ratio (MLR) Algorithm
Each iteration calculates the local ratio corresponding to 𝐷 ∈ 𝒟 in the current iteration state.
Choose the disk with minimum , which is marked by “*”, to cover TDs contained in
Update relevant variables.
= / min(, ), ∀𝐷 ∈ 𝒟.
Local Ratio:
← − min(, ), ∀𝐷 ∈ 𝒟.

## Slide 12
An Instance
𝑈 = {1, 2, ..., 20}, 𝐴 = {1, 2, 3, 4, 5} and 𝑘 = 5.

## Slide 13
Background
01
Experiments
03
Our Approach
02
Conclusion
04

## Slide 14
Experiment
Specific experimental settings
Two comparison methods
  NCA (nearest capable access)
  OPT (optimal solution)

## Slide 15
Experiment
Impact of the Number of TDs
The number of TDs gradually increases from 20 to 500, and all facilities are distributed in an area with a side length of 40. The ratio between the number of TDs and APs is maintained at 25:1, and the capacity of each AP is 𝑘 = 40. For the two constants in equation (1), the values are 𝑐 = 1 and 𝛼 = 2.
More power efficiency
Acceptable execution time
More harmonious assignment

## Slide 16
Experiment
Impact of 𝑘
𝑚 = 4 and 𝑛 = 100, side length is 40,
Benefits from increasing .

## Slide 17
Experiment
Impact of the number of APs with 𝑘 = 25
𝑚 = 4 and = 100, side length is 40,
More APs, lower power requirements

## Slide 18
Experiment
Impact of the number of APs with 𝐾 = 160
and = 160, side length is 40,
More APs, lower power requiements

## Slide 19
Background
01
Experiments
03
Our Approach
02
Conclusion
04

## Slide 20
Conclusion
We consider the signal coverage process in edge networks as a minimum power coverage problem and define this problem as an MPCC problem.
Modeling this problem in MEC.
We propose a local-ratio-based approach to solve the MPCC problem.
Contribution
Another approach to solve MPCC problem.
Considering heterogeneous APs and TDs’ natural number requirements (not just 1)
Future works

## Slide 21
Thank you for listening!

## Slide 22
Thank you for listening!